## Slide 1
IDEA :-Fixture design needs to change
TPM CIRCLE NO :- 01
TPM CIRCLE NAME: Oil Pump
DEPT :- ASSEMBLY SHOP
CELL :- A315
CELL NAME:- Oil Pump Assly
ACTIVITY
LOSS NO. / STEP
RESULT AREA
MACHINE / STAGE :- Free rotation stage
OPERATION :- Free rotation
KK
KAIZEN IDEA SHEET
QM
PM
JH
SHE
OT
DM
E&T
P
Q
A
C
D
S
M
KAIZEN THEME : To reduce rejection of plate shift in A315 oil pump.
Problem present status :-A315 plate shift found at final inspection stage.
COUNTERMEASURE:-
1) To get rigid resting fixture procured with three resting pins
BENCHMARK
TARGET
KAIZEN START
KAIZEN FINISH
1949 Nos
0 Nos
05.05.2016
20.05.2016
TEAM MEMBERS : Dipali Shete, Nitin Sutar
Mohan Kate, Bhavesh Pednekar.
BENEFITS :-
MANAGER’S SIGN :- Sandeep patil
REGISTERED BY :- Mohan kate
REGISTRATION NO. & DATE : 11.05.2016
WHY - WHY ANALYSIS :-
Why1 :-A315 plate shift found at final inspection stage.
Why2:-Inadequate fitment on screw in body
Why3 :-body tilt during screw fitment Why4 :-Uneven resting of body on fixture
Why4 :-Fixture design is not according to component
RESULT :-
KAIZEN SUSTENANCE
WHAT TO DO: Verification of three pins existence.
HOW TO DO: JH/ fixture PM
FREQUENCY –Daily /Monthly
P15
After
Before
ROOT CAUSE : Fixture design is not according to component.
B
Reduction in in-house rework
SCOPE & PLAN FOR HORIZONTAL DEPLOYMENT |  |  |  | 
Sr No | CELL | TDC | RESP. | STATUS
1 | All Casting |  | Mr. Nitin sutar | Completed
Only two pins available for component resting
Chart: Result Monitoring
| Before | After
 | 2123 | 0