## Slide 1
IDEA : No metal to metal contact
TPM CIRCLE NO :- 02
TPM CIRCLE NAME:
DEPT :-
CELL:-
CELL NAME:- Bracket SPM
ACTIVITY
LOSS NO. / STEP
RESULT AREA
MACHINE / STAGE :- A247 Bracket
OPERATION :- Drilling 4.2mm
KK
KAIZEN IDEA SHEET
QM
PM
JH
SHE
OT
DM
E&T
P
Q
A
C
D
S
M
KAIZEN THEME :To eliminate bracket SPM A1 machine breakdown
Problem present status :- 4.2 mm drill spindle frequent breakdown. 4 B/d / month and Apprx 250 minutes / month
COUNTERMEASURE:-
Replacing gear drive & key mechanism with modified Shaft & Taper locking pulley
BENCHMARK
TARGET
KAIZEN START
KAIZEN FINISH
245 min/ month
0
05.05.2016
10.06.2016
TEAM MEMBERS :
Prakash Harihar
Sujit Zirpe
BENEFITS :-
MTBF increased from 7.5 Days to
life time (PM planned @ 1 Year)
2) Production per month increased by1050
MANAGER’S SIGN :- SNC
REGISTERED BY :- Prakash & Sujit
REGISTRATION NO. & DATE :
WHY - WHY ANALYSIS :-
RESULT :-
KAIZEN SUSTENANCE
WHAT TO DO:-. Bearing replacement.
HOW TO DO:- During PM
FREQUENCY :- @ 12 months
P15
After
Before
ROOT CAUSE : Metal to Metal contact
Why 1 – 4.2 mm Drill spindle breakdown Why 2 – Spindle jammed Why 3 – Play in transmission gear Why 4 – Key between shaft& gear wear and tear. Why 5 – Forced deterioration due to metal contact.
Worn out key way
Worn out key
Chart: Breakdown time status
| Jan ~ Apr 16 | May-16 | Jun-16 | Jul-16
 | 930 | 245 | 0 | 0
Drill spindle b/d phenomena eliminated
Availability of machine increased by
245 min / month
Taper locking pulley
Modified shaft and tapered locking pulley mechanism